## Slide 1
Fuel Tank
Solar Cells
Docking Port
High-Gain Antenna
Hub

## Slide 10
ATTITUDE STATE REPRESENTATION
class Spacecraft():
ORBIT STATE REPRESENTATION
Spacecraft.states
Spacecraft.elements
*XYZ coordinates in ECI (J2000) frame
*Equivalent orbital elements (osculating)
*Mutually updated for state consistency
Spacecraft.attBN
Spacecraft.attBR
Spacecraft.ohmBN
Spacecraft.ohmBR
*Body to inertial attitude (coordinate agnostic)
*Body to inertial angular velocity (body-frame)
*Body to reference attitude (coordinate agnostic)
*Body to reference angular velocity (body-frame)
ORBIT PROPAGATION METHODS
ATTITUDE PROPAGATION METHOD
Spacecraft.propagate_orbit(self, dt)
Spacecraft.propagate_orbit(
  self, t, dt, integrator='RK4')
*Keplerian-only analytical two-body propagator
*Numerical propagator (default RK4), with references to own force models
Spacecraft.propagate_attitude(
  self, dt, torque)
*Torque as a 3x1 vector applied in body-frame coordinates